## Interim Certification to 38/03

- Prior to SE forms becoming available, submissions to ADR 38/03 using a UNECE approval should consist of a blank form set to ADR 38/03, reporting the full approval number and whether the trailer is designed for road train combinations. If it is designed for road train combinations it must report the release time at the rear service coupling which must be less than 650 ms. It must also report compliance to clauses 6.7 Antilock (where applicable) and 8.2 Mechanical parking system.

- Submissions to ADR 38/03 using the calculation method should generally consist of a blank form set to ADR 38/03, with the 38/02 form type (SE 38/02 TB, SE 38/02 CS etc) relevant to the submission attached.

- The exceptions to this are the SARN 38/…., the SE 38/03 FB and the SE 38/03 SS, which only need the form type as available in the /02 version (no additional blank form).

- The blank forms set to 38/03 should be filled out according to whether a variable proportioning brake system is fitted, as shown below:

### ADR 38/03 without variable proportioning brake systems

- SE 38/03 TB and SE 38/03 – on the blank form state;

“Variable proportioning brake system not fitted, as per Clause 22.3”

- SE 38/03 CS – on the blank form state;

“Variable proportioning brake system not fitted, as per Clause 22.3”

“Designed to be used in ‘Road Train’ combinations” or

“Not designed to be used in ‘Road Train’ combinations” as applicable.

### ADR 38/03 with variable proportioning brake systems optionally fitted

- SE 38/03 TB – on the blank form state;

“Variable Proportioning Brake system optionally fitted”

“Minimum UTM = “ XX “tonnes” (must be less than the smallest reported GTM on the SE 38/02 TB)

- SE 38/03 CS – on the blank form state;

“Variable Proportioning Brake system optionally fitted”

“Minimum proportioning valve output/input ratio for compliance = YY

“Proportioning valve part numbers”

ZZ

AA

BB etc

“Designed to be used in ‘Road Train’ combinations” or

“Not designed to be used in ‘Road Train’ combinations” as applicable.

- SE 38/03 – on the blank form state;

“Variable Proportioning Brake system optionally fitted”

“Meets both Figure 2 unladen and the transition to Figure 1”

“Minimum UTM =” CC “tonnes” (must be less than the GTM)

“Copy of the markings required by clause 6.8 are attached.” (and attach a copy)

Note 1: The attached copy must cover all trailers within the variant (worst case) but need not be the markings that appear on any particular trailer. Multiple attachments may be provided.

- When using the SE 38/02 form;

In filling out the table on page 2 of the SE 38/02 form, complete the table for the combinations of tyre radius as applicable.  If only one tyre radius used, complete the first row. If more than one tyre radius used, complete both rows. There is no reference to permit masses required as there are no axle load limits in the ADR for these systems.

# Footnotes

This allows a trailer variant to be fitted with a variable proportioning brake system as either standard or optional, at the manufacturer’s discretion.